## Slide 1: 5G NB-IOT
Presentation 2021-2022
October, 15
UNDER THE GUIDANCE OF
Prof. Daniela DRAGOMIRESCU
Yacine BENCHEHIDA – Hugo LE BELGUET – Sami BEYAH 5ISS

## Slide 2: Contents
I- Introduction
II- Physical Layer
III- Mac Layer
IV- Power consumption
V- Security
VI - Conclusion

## Slide 3: I- Introduction
A new IoT technology introduced by the 3GPP in 2016
Reuses the LTE design extensively
A support of a massive number of connections (up to 50,000 per NB-IoT network cell)
It eliminates the need for a gateway, which saves cost in the long run
Minimises power consumption enabling battery life of +10 years

## Slide 4: II- Physical layer
Maximum Data rate in uplink :
        250 kbps (multple itone)
        20 kpbs (single tone)
Coverage :
        1 km in urban area
        15 km in rural area
Uplink report latency : < 10 s
Applicable in any 3GPP defined (licensed) frequency band
Bandwidth : 180 kHz
Uplink and downlink communication in half duplex
Three deployment modes
Source : https://www.netmanias.com/en/post/blog/11745/iot-nb-iot/nb-iot-the-choice-of-frequency-deployment-mode-and-coverage

## Slide 5: II- Physical layer
Supports two modes for uplink :
        Single tone with 15 kHz and/or 3.75 kHz tone spacing
        Multiple tone transmissions with 15 kHz tone spacing
Source : An open-source platform for exploring NB-IoT system performance
Source : NB-IoT Networks by ITU

## Slide 6: II- Physical Layer
Low Power Wide Area Network (LPWAN)
Example of a constellation Diagram for BPSK
Source : https://blog.integral-system.fr/quest-ce-que-nb-iot/

## Slide 7: II- Physical Layer
In Uplink, the modulation used is :
For single-tone, the modulation is π/2-BPSK or π/4-QPSK
For multitone it is always QPSK.
This improves the power-amplifier efficiency cost in the mobile terminal at lower data rates

## Slide 8: II- Physical Layer
NB-IoT supports ultra-low complexity devices with very narrow bandwidth, 200 kHz.
Rural area | Urban area
10 km | 1 km
Handover 🡪 End-devices join a single base station
Data Rate & Scope
Due to its narrow bandwidth, the data rate peaks at around 20 until 250 Kbits/s.
Channing Coding 🡪 Turbo codes

## Slide 9: III- Mac Layer
For Downlink communications, OFDMA is used
🡪 Resistance to interference
🡪 Reduction of multipath fading effects
For Uplink communications, the access protocol is SC-FDMA.
🡪 Reduction of inter-symbol interference
In NB-IoT, the access protocols are different between uplink and downlink.
Source : https://blogs.univ-poitiers.fr/f-launay/tag/ofdm/
Source : https://www.researchgate.net/figure/Difference-entre-OFDMA-et-SC-FDMA-6_fig4_308266132

## Slide 10: III- Mac Layer
Physical signals and channels

## Slide 11
III- Mac Layer
To avoid collisions on the NPRACH channel, NB-IoT use the Slotted ALOHA protocol.
Collisions
The main characterizes about this protocol are:
• Slotted Aloha divides the time of shared channel into discrete intervals called as time slots.
• Any station can transmit its data in any time slot
• The only condition is that station must start its transmission from the beginning of the time slot
• If the beginning of the slot is missed, then station has to wait until the beginning of the next time slot
• A collision may occur if two or more stations try to transmit data at the beginning of the same time slot

## Slide 12
NB-IoT mechanism
Extended Discontinuous Reception (eDRX)
Power Saving Mode (PSM)
Extended Coverage Level (ECL)
Realease Assistance Indicator (RAI)
Source : The Low Power Modes of the Cellular IoT by Thales Group
IV- Power consumption

## Slide 13
Transmit measure realised with a 23 dBm signal
Sleep corresponds to eDRX mode
Standby corresponds to PSM mode
Device A is commercially available
Device B is a prototype
With 100 bytes packet and a 27,7Wh battery size
Power consumption
Measurement of an NB-IoT power consumption
Source : An Empirical NB-IoT Power Consumption Model for Battery Lifetime Estimation by Lauridsen, Mads; Krigslund, Rasmus; Rohr, Marek; Madueno, Germán
IV- Power consumption

## Slide 14
Non-IP data delivery :
Via PtP Sgi Tunnel, can only communicate with a pre defined server
Via SCEF, new network element that securely exposes the server and capabilities provided by 3GPP network interfaces
DoNAS encapsulate the data of the user in the Non-Access Startum
Uses the LTE existing network, benefits from its security:
User identity confidentiality
Entity authentification
Data integrity
Mobile device identification
Source : Security Features of LTE-M and NB-IoT Networks by GSMA
V- Security

## Slide 15
VI- Conclusion
NB-IoT was designed to allow easy integration and sharing of radio resources with existing GSM and LTE networks
This technology have several advantages :
              It focus on energy efficiency
              Indoor/underground penetration
              Massive IoT connections
              It benefits from all the security and privacy features of mobile networks
By using licensed spectrum it provided greater reliability and performance
NB-IoT is seen as the future of IoT devices using mobile network infrastructure